## Slide 1
Department of Electrical and Computer Engineering (ECE)
Digital Dash
Portland State University
Sean Koppenhafer, Jaime Rodriguez,
Chad Thueson, Noah Erickson, Rishal Dass
Notes: 1
1

## Slide 2
Electric systems add complexity and a traditional LED dash won't suffice
Drivers must be aware of system faults and warnings
An LCD Dashboard must be created to accommodate additional electrical systems
Formula SAE Electric Car
Current Traditional LED Dash
Project Overview

## Slide 3
Progress
Completed
Arduino can get RMS and BMS data
Screen can output BMS and RMS data
Prototype software and hardware works completely
Lots of documentation
Still to accomplish
Assemble final board
Program final board
Assemble the demo unit
Create enclosure

## Slide 4
Block Diagram

## Slide 5
Software
Arduino Code
Searches for specific CAN message ID’s, specified in code
Sends messages via serial to the screen module (uses a visi-genie library)
Currently running on an Arduino Due but will port over to the custom PCB
4D Visi-Genie
Controls the positioning of the gauges, bars and symbols
Handles button presses and their submenus
Scales code sent from Arduino Due to match output data

## Slide 6
Screen Module
4D Systems uLCD-35DT
  3.5” Resistive Touch Screen
  Display Module handles graphics processing and image storage
User Interface
  IMD, BMS and Motor symbols act as buttons to get into submenus
  Battery level, Motor
  temp and amperage
  displayed

## Slide 7
Enclosure Designs
?

## Slide 8
Power & Can Transceivers
  The CAN transceivers receive data from the BMS and RMS and send them to the Arduino Due
  Power Board steps 12V down to 5V also includes CAN transceiver circuitry
    The TLF1963 Voltage runs very hot
    May end up just using 5V from GeVCU
Arduino Due
  Runs the software for processing CAN messages and mapping them to the screen module
Prototype Boards

## Slide 9
Simple enclosure for track day testing
  Mounted to the driver side pod to eliminate blind spots
  Track day enclosure is also water resistant
  Arduino Due, power board and screen secured in box
  This enclosure was quickly created for a track day prototype and is not intended for the final unit
Prototype Enclosure

## Slide 10
Why a custom PCB?
  Cut down on total dash board size
  Designed to plug directly into the back of the screen module
Components
  Contains the essentials of an Arduino Due and the prototype power board with CAN transceivers
Other Details
  Manufactured by OSH Park
  3 boards were manufactured
Custom PCB
Include a side by side picture of the Arduino Due size vs PCB

## Slide 11
Requirements
  Waterproof
Dimensions
  Must be low profile to fit in dash
  Viewing angle is a bit awkward, through the steering wheel
Final Enclosure

## Slide 12
Unit Created to Simulate Car
  Runs off the Arduino Due used for prototyping
  Will be used to demonstrate project
Hardware
  Potentiometers and buttons to simulate functionality of the car
Software
  Sends input data from potentiometers and buttons to the digital dash unit
Demonstration Unit