## Slide 1: Digital Dashboard Capstone
Team Members: Sean Koppenhafer, Jaime Rodriguez,
Chad Thueson, Noah Erickson, Rishal Dass
Notes: Slide Purpose: Introduce ourselves

## Slide 2: Project Overview
Electric systems add complexity and traditional LED dash would not suffice
Drivers must be aware of system faults and warnings
A Digital Dashboard must be created to accommodate additional electrical systems
Formula SAE Electric Car
Traditional LED Dashboard
Notes: Slide Purpose: What did we have to do

## Slide 3: Requirements
Size
Price
Reproducible
User-Friendly
LCD Screen < 4”
Custom PCB
LCD Screen < 4”
Arduino Based
Arduino Based
Arduino Based
Custom PCB
LCD Screen < 4”
LCD Screen < 4”
Notes: Slide Purpose: Show requirements linked to decisions

## Slide 4: Consideration – Microprocessor
 | Cost | Custom Board | CAN Controller | CAN Library | SPI, I2C, UART, etc
ATMEGA328 | $3 | Yes | No | No | Yes
AT90CAN | $8 | Yes | Yes | Yes | Yes
Arduino Uno | $25 | No | No | No | Yes
Arduino Due | $50 | No | Yes | No | Yes
ATSAM3X | $12 | Yes | No | Yes | yes
The ATSAM3X was chosen with the following consideration:
Custom PCB
External MCP-2551 CAN Transceivers
ATSAM3X
4DSystems LCD
Digital Dashboard
CAN Communication
Notes: Slide Purpose: Why we chose the ATSAM3X

## Slide 5: Consideration – Screen
 | Cost | Size | Color | Visibility | Software
EarthLCD | $219 | 3.5” | Yes | Yes | Yes
New Haven | $60 | 4.9” | No | Yes | No
Sun LCD | ??? | 3.5” | Yes | Yes | No
4D Systems | $89 | 3.5” | Yes | No | Yes
The 4D Systems Screen was chosen with the following consideration:
Overdriven Display Voltage
Polarizing Shield
ATSAM3X
4DSystems LCD
Digital Dashboard
CAN Communication
Notes: Slide Purpose: Why we decided on the screen

## Slide 6: Consideration – Comm. Protocol
 | Complexity | Available |  | 
I2C | Simple | Yes |  | 
SPI | Simple | Yes |  | 
CAN | Complex | Yes |  | 
Wi-Fi |  | No |  | 
ATSAM3X
4DSystems LCD
Digital Dashboard
CAN Communication
Notes: Slide Purpose: why we decided on CAN
CAN was already implemented

## Slide 7: System Overview
GEVCU
CAN Buses
Power Supply
Microcontroller
LCD Screen
Notes: Slide Purpose: Show how the system connects

## Slide 8: Printed Circuit Board
Features
Small Size
2-Layer Designed for easy reflow
Multiple Power Supply Inputs
Flush Mating Header
Inputs
5V or 12V Power
Outputs
LCD Mating Header
Programming Port
CAN Bus 1 High and Low
CAN Bus 2 High and Low
CAN Inputs
LCD Mating
Header
Programming Circuit
12V Supply
Functionally an Arduino Due
Notes: Slide Purpose: Show off our awesome PCB

## Slide 9: Software
Format is .ino
Can be uploaded via programming port and Arduino IDE
Notes: Slide Purpose: Show off our awesome software

## Slide 10: GUI
4D Systems ViSi-Genie
High contrast for quick interpretation
Touch enabled subscreen buttons
Main Screen
BMS Subscreen
Notes: Slide Purpose: Show GUI decisions

## Slide 11: Testing
Notes: Slide Purpose: Talk about demo unit?

## Slide 12: Programming
Mainboard
  Disconnect the 4D Systems LCD
  Connect the external programmer to the programming port
  Upload desired code via Arduino IDE
4D Systems LCD
  Disconnect the 4D Systems LCD
  Connect the external 4D Systems Programmer
  Upload desired code via 4D Systems ViSi-Genie
  Upload desired GUI to 4D Systems microSD card
Notes: Slide Purpose: Show how easy it is to reprogram

## Slide 13: Reproducibility
Notes: Slide Purpose: Show how to reproduce a unit

## Slide 14: Documentation
Reproduction Instructions
Development Team Biographies
Development Team Progress Meetings
Development Roadblocks and Milestones
Budget and Schedule
Test Plans
Notes: Slide Purpose: Show what documentation we have

## Slide 15: Future Revisions
Revision 2.0
Software
Enclosure
Mainboard
Polling Based
Smaller
Programming Circuit
Power Supply
LCD Header
Notes: Slide Purpose: Show what we could improve

## Slide 16: Conclusion
Notes: Slide Purpose: wrap this up